## Slide 1
Perishable transport

## Slide 2: Agenda
Goal and definition
Legislation
Sustainability
Different concepts within road transport
Used techniques in cooling
Intermodal transport

## Slide 3: Perishable transport
Perishable transport is transport of (perishable) goods within a controlled atmosphere to avoid unnecessarily loss of quality of the product.

## Slide 4: Perishable transport
Flowers and plants
Vegetables and fruit
Meat
Dairy (zuivel)
Foodproducts (including fish)
Examples:
Milk : cooled
Fish : cooled or frozen
Chocolate heated
Turnover of perishable transport in Holland: 1 bil Euro

## Slide 5: Perishable transport
Cooled
Heated
Ventilated
Furthermore……
….avoiding contamination
….check of the cargo
…..combined cargo/temperature possible

## Slide 6: Perishable transport
 | plus | minus
airfreight | high speed | no water allowed
 | low volume / weight | high price
roadtransport | flexible | double crew /limited driving time
 | FTL/LTL | cooling by diesel
 | guarded transport | 
railtransport | timetable | speed
 |  | unguarded transport
 |  | cooling bydiesel / nu surveillance
barge/shortsea | timetable | speed
 | guarded transport | 
 | low price cooling by electricity | 

## Slide 7: Reefers
Temperature range from -30 until +30
So, it can heaten too !
Walls, floors and ceilings are made of isolated material.
Truck with side curtains: only for cooled products until freezing point.

## Slide 8: Atmosphere
Modified Atmosphere (MA)
Standard Atmosphere inside packaging
21% oxygen and 0,03% carbon dioxide
Controlled Atmosphere (CA)
Composition as desired
LO (low oxygen about 2%)
ULO (Ultra low oxygen < 2%)
Example:
Apple 
high speed of respiration 
reduce oxygen 
lifetime prolongation

## Slide 9: Methods of cooling
With generator (intern)
With generator (extern)
Without generator
Cooling with ice.

## Slide 10: Transport temperatures
Fish: frozen -180
fresh on ice -20
Meat: fresh + 20
frozen -100
Consumption ice -240
to avoid crystallisation

## Slide 11: New developments
Airfreight will become less important due to alternatives
Speed can/will be reduced by intensive monitoring
Growth of plants will continue during transport
PPO (Applied plant research dept. situated in Wageningen, Holland) is a leading organisation in these kind of developments

## Slide 12: Legislation / rules
Together we have made the following arrangements ……

## Slide 13: ATP: Accord Transport Perissables
ATP is valid for international transport of deeply frozen, cooled and heated products.
ATP describes frameworks for:
  Insulance (isolatiewaarde) of the cargo space
  Temperature range of the cooling device.

## Slide 14: HACCP: Hazard Analysis and Critical Control Points
HACCP is a checking system to secure the constant quality of food and the safety of food. This all for the consumer.
HACCP is valid as from production until consumption including transport and storage.
The system is developed and checked by the market itself.

## Slide 15: Essential points of HACCP
The 7 essential points of the HACCP – system are:
  Inventory all potential dangers:
  Determine the Critical Control Points (points within the process where risks can be prevented or limited);
  Determine the critical limits per CCP and determine how they can be guarded or monitored.
  Determine the corrective actions what will lead to return to safety;
  Use verification as a periodical check to see if HACCP still works properly.
  Document and record everything you have adapted and how.

## Slide 16
Perishable transport: assets
With cars who have an isolated loading space and a cooling device

## Slide 17: Perishable transport: various assets/concepts

## Slide 18: International: truck + semi-trailer

## Slide 19: International: truck + trailer

## Slide 20: National: truck + trailer

## Slide 21: National: LHV

## Slide 22: Distribution: Trailer

## Slide 23: Distribution: city semi-trailer

## Slide 24: Distribution: delivery van

## Slide 25: The sustainable refrigerator
The sustainable refrigerator……
……………. makes a minimum of noise (with full power)
…………….uses a minimum of power or fuel
…………….has a minimum of maintenance
…………….emits a minimum of emission
……………. is as light as possible.

## Slide 26: Drive concepts of the cooling device
Direct driven
Cooling by C02 or nitrogen (stikstof)
Diesel-compressor driven
  Diesel-generator driven
  truck-generator driven
  Hydraulic-electric driven
Truck engine
compressor
Heat exchanger
Direct injection
Truck engine
Diesel engine
Heat exchange
compressor
Truck engine
Diesel engine
Heat exchange
compressor
Generator
Truck engine
Heat exchange
compressor
Generator
hydraulic
Heat exchange
compressor
Generator
Truck engine
Truck engine
Not in the concept
In the concept

## Slide 27: Direct driven
Only for small vehicles like vans.
Compressor is directly fixed to the engine of the van.
Advantages:
cheap
light
simple and reliable
minimum of maintenance
low cost of ownership
Disadvantages
limited power available
with a stationary engine the efficiency is minimum
average performance by constant fluctuating number of revolutions
of the engine.
Truck engine
compressor
Heat exchanger

## Slide 28: Suppliers of direct driven compressors

## Slide 29: CO2 or nitrogen (stikstof) drive/cooling cryogenics: is the study of the production and use of very low temperatures
A fluid gas will be insulated in the cargo space or heat exchanger. Due to evaporation the temperature will decrease.
Advantages:
very low noise emission
long lifespan
little maintenance
due to sustainability it is one of the best solutions
Disadvantages:
high cost of ownership
variable cost depends on the current price of gasses
just a few tank stations (in Holland 3-4)
storage tank is heavy and takes a lot of space
dangerous. CO2 is a toxic and heavy gas.
Direct injection

## Slide 30: Suppliers of nitrogen cooling
Thermo King is the only
supplier and also supplier for Dasko.
Cryo tech-unit

## Slide 31: Diesel -compressor driven
The diesel engine drives the compressor,
normally by using belts or V-belts.
Advantages (of diesel driven)
Cooling device works independent
from the truck
reliable technique
relative low purchase price
Disadvantages (of diesel driven)
industrial diesel engines emit 10-60x more pollution than truck engines
higher use of fuel than truck engines
higher noise pollution than truck engines
engines are heavy and big
demand a lot of maintenance
Diesel engine
Heat exchange
compressor

## Slide 32: Diesel - generator driven
The diesel engine is connected to the generator.
The generator delivers power
The power is used for the electric compressor.
Diesel engine
Heat exchange
compressor
Generator

## Slide 33: Suppliers of diesel driven systems

## Slide 34: Diesel-generator driven
The generator is connected to the truck engine and delivers power for
the refrigerator.
Advantages:
low use of fuel
low noise pollution
low cost of ownership
Disadvantages:
cooling power dependable of the number of revolutions of the engine
often the only way to connect both devices is by V-belt
generator can have problems with its temperature (lack of air flow)
Truck engine
Heat exchange
compressor
Generator

## Slide 35: Suppliers of direct driven generators

## Slide 36: Hydraulic- electric driven
The engine of the truck is connected to a hydraulic system.
The hydraulic systems is connected to the generator
The generator supplies power for the refrigerator.
Advantage:
low use of fuel
power undependable of the number of revolutions of the truck engine
low noise pollution
communication via motor management of the truck possible
Disadvantage:
high purchase costs
Hydro pump hydraulic generator
hydraulic
Heat exchange
compressor
Generator
Truck engine

## Slide 37: Trade off: price versus sustainability

## Slide 38: Future ?
The refrigerators will be driven by:
  fuel cell
  LNG / CNG / Biogas
  engine of the truck
  braking energy of the truck replenished with solar energy.
  The use of the truck engine will remain one of the best alternatives due to the latest emission directives, hybrid solutions, CNG, LNG and Biogas

## Slide 39
Intermodaal

## Slide 40: Airflow in a reefer container

## Slide 41: Refrigerate units
Clip-on built-in

## Slide 42: 45ft PW HC reefer
Internal measurement 13,275 mtr suitable for 33 euro pallets
(45ft container = 13.60 meter trailer)
Double stack system possible
Perfect for rail and barge
Temperature can be controlled and changed on distance via micro processor
Double stack

## Slide 43
45 ft PW HC dual/triple compartment reefer
with variable temperature zone

## Slide 44: Is this tank container suitable for perishable goods?
This is a container for dangerous goods, so……